## Slide 1
Panasonic Industrial Devices Automation Controls Sales Asia Pacific
FP-7 Programmable Controller Multi Input/Output unit

## Slide 2
All Rights Reserved © Panasonic Corporation
Features
Performs multiple functions with a single unit

## Slide 4
AFP7MXY32DWD (Standard type)
16 digital inputs
Normal i/p
Hi Speed Counter
Interrupt i/p
Signal
Sink or source (4 to 1 common)
5/12/24 Vdc
Time filter configurable
Hi Speed Counter
- 4 channels
- 3 modes
500kHz, 5Vdc
250kHz, 12-24V
Interrupt
- 8 points
External signal or comparison match
16 digital outputs
Normal o/p
Pulse
PWM
Comparison
Signal
sink, source, push-pull
5-24 Vdc
Pulse
4 channels*
500kHz (50% Duty)
3 modes
Jog (w/o or c/w target)
PWM
4 channels
100kHz
Comparison
8 points

## Slide 5
Difference between Standard and Positioning

## Slide 6
B E F O R E |  |  |  | TR series’ 12V encoder outputs requires additional TR controllers
A F T E R |  |  |  | Since the Multi I/O Unit can accept 12V signal from encoder outputs, controllers is not necessary
12V
Encoder output
24V
Transistor output
12V
Encoder output
Digital I/O
Multi I/O
TR-C21R-S
Encoder output connected directly
Cost saving
TR Series
Accepts 5 to 24 V input. Lower cost without the need for controllers (converters)
Inputs

## Slide 7
Configuration of unit can be easily performed using the Setting tool
Setting tool and Template in FPWin-Gr7
Template allows programmers to select the UM address without referring to manuals

## Slide 8
Setting Tool

## Slide 9
Setting Tool

## Slide 10
Template

## Slide 11
Comparison
(HSC)
Biggest difference between Multi I/O Unit and High-Speed Counter Unit is input of HSC supports differential input
As such, 16 MHz measurement is possible with differential input.
For measuring in the few hundred kilohertz range, the Multi Input/Output Unit can be used.
Multi I/O Unit is a better option than HSC2T when application requires more than just HSC
(This is because unused counter channels of MIO can be used as general-purpose I/Os )

## Slide 12
Comparison
Positioning

## Slide 13
Comparison
Pulse

## Slide 14
Application Examples
Feature packed unit with easy interface to :-
Measuring instrument and/or equipment tester with 5V output
Motor/inverter control
Dedicated board peripherals

## Slide 15
Next…
FP-XH

## Slide 16
Inputs